## Slide 1: WIB Firmware Development for DAT ColdADC ENOB QC
Jillian Donohue on behalf of the BNL CE group
Date TBD
Notes: Title: WIB Firmware Development for DAT ColdADC QC

## Slide 2: Outline
ColdADC ENOB QC requirements
Single channel buffer firmware
ENOB results
To-do list

## Slide 3: ColdADC QC requirements
Requirements:
  Sampling frequency ~2 MHz
  Number of ADC bits: ≥ 12
  Total power (of all ASICs): < 50 mW/channel
  Noise contribution ≪ 1000 e- (negligible compared to LArASIC)
Specifications:
  Crosstalk: < 1%
  Differential Nonlinearity (DNL): Absolute value < 1
  Integral Nonlinearity (INL): < 1(12-bit ADC unit)
  Equivalent Number of Bits (ENOB) > 10.3
  Overflow protection: When input signal exceeds the upper or lower ADC range, the output should be fixed at the maximum or minimum value.

## Slide 4: ColdADC QC Procedure and Test Items based on DAT
Chip Placement
(manual or Robot)
Record input info
Input info: Date, Time, Location, Tester, DAT SN, Socket SN, Chip ID, and etc.
Placement checkout
(<1 min)
PASS?
QC testing (RT & LN2)
Basic functionality checkout to assure any chip is aligned in the socket, no short, no open pin
Y
N
Power cycle at least 5 times with different configs
Test I2C communication (Write/read registers)
Check power-on reset (verify default register values)
Measure reference voltages
Perform auto calibration; check weights
Measure open channel noise (new DAT)
Measure DNL/INL (slow ramp or sine wave input)
Check overflow protection
Measure ENOB (optional)
Measure ring oscillator frequency
Crosstalk (optional, performance to be evaluated)
Verified doable on DAT

## Slide 5: ENOB requirements
> 4,000 [?] samples
  Spy buffer only can store ~2000 samples per channel
Others?

## Slide 6: Firmware additions
DAQ modified frame builders
x8
Accumulators
x8
Histogram
AXI BRAM controller
Live data peek reg.
Single channel buffer

## Slide 7: Single channel buffer firmware module
deframed_data_aligned
Single channel buffer
state machine
16-bit channel data
User controls:
Trigger
Channel to analyze
rq_state x 8
(indicates data is verified & ready)
fbld_modified
Buffer full
BRAM memory
2^13 32-bit regs.
Channel data
AXI bus

## Slide 8
deframed_data_aligned
Single channel buffer
state machine
16-bit channel data
User controls:
Trigger
Channel to analyze
rq_state x 8
(indicates data is verified & ready)
fbld_modified
Buffer full
BRAM memory
2^13 32-bit regs.
Channel data
AXI bus

## Slide 9: Repurposing histogram memory
Single channel buffer
Histogram
BRAM memory
2^13 32-bit regs.
AXI bus
AXI BRAM controller
Reg-controlled mux
0
1
hist_buf_sel
R/W signals

## Slide 10: Results

## Slide 11: WIB registers used – config register bank
0xA00C0078: Histogram channel to analyze, lemo_io_0 output selector
0xA00C007C: Histogram # samples
Address, hex | Bits in register | Parameter name | Description
0xA00C0070 | 28:10 | accum_num_samples | Number of samples to accumulate
0xA00C0070 | 9:1 | accum_total_ch_sel | Accumulator channel readout selector. Channel X's accumulated total will appear in the register accum_ch_total if you write X to this register.
0xA00C0070 | 0 | accum_trig | Triggers accumulators to begin
0xA00C0074 | 1 | hist_buf_sel | Determines whether the AXI BRAM controller (0) or the single channel buffer (1) has access to port B of the histogram BRAM
0xA00C0074 | 0 | hist_buf_trig | Triggers histogram (0) or single channel buffer (1) to begin, depending on the value of hist_buf_sel
0xA00C0078 | 8:0 | hist_ch | Channel to take histogram (or single channel buffer) data for
0xA00C007C | 31:0 | hist_num_samples | Number of samples to count for histogram
Latest production firmware uses config registers up to 0xA00C0044
Notes: Can be changed if needed (secondary register bank to minimize use of main registers, could bring it down to 2ish registers (one config and one status)?)

## Slide 12: WIB registers used – status register bank
Latest production firmware uses status registers up to 0xA00C00D8
Address, hex | Bits in register | Parameter name | Description
0xA00C00F0 | 23:10 | deframed_data_mon | Allows software to “peek” into the live channel data to aid the histogram test (hist_ch determines which channel)
0xA00C00F0 | 9 | hist_ready | Indicates that the histogram has finished taking samples
0xA00C00F0 | 8 | buf_done | Indicates that the single channel buffer has finished taking samples
0xA00C00F0 | 7:0 | accum_ready | Bit Z indicates that accumulator Z (connected to COLDATA Z) has finished taking samples
0xA00C00F4 | 31:0 | accum_ch_total | Displays the total accumulated in channel accum_total_ch_sel when its accumulator is finished
0xA00C00F8 | 31:0 | hist_out | Was used for peek-by-peek readout of histogram data, but no longer used.
Notes: Can be changed if needed (secondary register bank to minimize use of main registers, could bring it down to 2ish registers (one config and one status)?)

## Slide 13: Resource utilization update
Production firmware:
QC firmware (difference from last version):
(+1%)
(+4%)

## Slide 14: To-do list
  1. Histogram study with a sine waveform instead of a ramp
2. ENOB study
3. Develop analysis scripts for ADC static performance metrics
  DC-offset, input range, gain, DNL/INL, overflow protection, and etc.
4. Organize a QC procedure – scripts, database, etc.
Notes: ENOB technically optional?

## Slide 15: Summary
Histogram development & study with a slow ramp signal is done
DAT board has been deemed capable for ColdADC QC
  All necessary QC items have been verified
  New DAT revision will inject test pulse to each channel independently

## Slide 17
DAQ modified frame builders
x8
Accumulators
x8
Histogram
AXI BRAM controller
Live data peek reg.
Single channel buffer

## Slide 18: AXI memory mapping
To speed up readout of histogram data, I implemented a AXI BRAM controller in the firmware’s block design that accesses one side of the histogram dual-port block memory
Histogram BRAM
Direct R/W
AXI BRAM controller RO
AXI bus
Linux
Histogram
Port A
Port B
“Port B”
histogram data
2^14 x 16 bits = 32 KB BRAM
Notes: Don’t need to explain in detail
AXI BRAM/Petalinux side CAN write, useful for debugging purposes, but it doesn’t need to in this application

## Slide 19: AXI memory mapping
Notes: Reg_bank_64 originally spanned memory from A00C0000 until A00D0000. Reg_bank_64 uses only 128 bytes total of its 64KB allocated memory, so I decreased that allocation to 32K and squeezed in the AXI BRAM controller at A00C8000.
I couldn’t just squeeze it in between spy buffers because the kernel has to know that the memory is mapped to something, the spy buffers use all of their allocated space, and I didn’t want to have to change the kernel. This is also the reason I can only read out 1 channel at a time

## Slide 20: Histogram results
ColdADC code counts
1 second ramp from 0 to 2.2V, 1,639,000 samples/channel
ColdADC code
Counts per code
Notes: To add: more detailed analysis?

## Slide 21: Histogram results
ColdADC code
One plot of a channel when ADC is calibrated
One plot of a channel when ADC is uncalibrated
ColdADC code counts
1 second ramp from 0 to 2.2V, 1,639,000 samples/channel
Single channel, calibrated
Single channel, uncalibrated
ColdADC code
Counts per code
Counts per code
Further analysis is undergoing to extract some ADC DNL/INL
Notes: Missing codes should show up in uncalibrated

## Slide 22: Spy buffer vs. histogram comparison
ColdADC Readout w/ No Pulse
Notes: Early proof-of-concept histogram graphs (mostly just a fun demonstration)

## Slide 23: Backup slide: Vivado firmware schematic
deframer
fbld
modified fbld
histogram
accumulator
Zynq

## Slide 25: Accumulator software (still in development)
Procedure:
Set DAT registers so that ADC channels are connected to the ADC DAC
Set DAC to 0 LSB
Set number of samples to take
Trigger the accumulators
When accumulators finished, read channel totals out one by one
Set DAC to 1 LSB
…etc.
Command line:
root@dune-wib:~/BNL_CE_WIB_SW_QC# python3 adc_dac_cal.py
python3 adc_dac_plot.py tmp_data/ADCcal_02_10_2021_06_19_06.bin
Notes: Channel X total will appear in the totals register if you write X to a certain other register

## Slide 26: Histogram software (still in development)
Procedure (after hardware setup):
Set WIB register so that P8 LEMO input is sent over data cable to the DAT
Set DAT registers so that ADC channels are connected to WIB external signal
Set channel_to_analyze to 0
Wait until live channel monitor register equals 0x0000
Trigger histogram
When histogram indicates it’s finished, copy the histogram block of memory
Set channel_to_analyze to 1
…etc.
Save the copied data to a .bin file or similar
Command line:
root@dune-wib:~/BNL_CE_WIB_SW_QC# python3 adc_hist.py 1639000
python3 adc_hist_plot.py tmp_data/ADChist_22_09_2021_06_02_19.bin
Notes: The way the histogram data is copied is the same way that the spy buffer data is copied (memcpy)
This greatly speeds up execution time compared to peek/poking one by one
Will go into how I implemented this later

## Slide 27: Faster spy buffer decoding using DUNEDAQ C++ software
Initial WIB Ethernet (HERMES) frame decoding was done with Python (very slow)
Downloaded source code necessary for decoding frames to WIB
Compiled .so library file for WIB
Wrote script for generating a Windows or Linux library file for off-WIB analysis
Sped up decoding time of one frame from a few seconds to instantaneous
Notes: What is the exact speedup figure?